## Slide 1: WES237B: Software for Embedded Systems
Pat Pannuto
Department of Computer Science and Engineering
University of California, San Diego
Summer Session 2022

## Slide 2: Today
Morning
  Performance & Optimization
  Optimization in different levels (in the context of a single core)
    Algorithmic (Cache Optimization), Compiler and Hardware
    Memory Hierarchy
Afternoon
  Lab session
    Applying optimizations: Loop unrolling, hardware vectorization (NEON)
    FIR Filters

## Slide 3: Logistics
Assignment 2 due tomorrow
Assignment 3 released
  Generally: First bit of assignment is lab portion, the rest is take-home
  Finish the lab first if needed
Late policy?
  1 week: 10% off
  2 weeks: Last chance, 30% off
  Email with any exceptional circumstances, we’ll work it out

## Slide 4: Recap
Measuring Performance
  Speedup / performance always relative and workload specific
  Amdahl’s Law: Optimization benefit limited to proportion it improves
Optimizations
  Hard & Getting Harder due to heterogeneity
  Must learn systems-level design and analysis
Microarchitecture
  ILP, Superscalar, SIMD, and Pipelining
  (perf: throughput)
Memory Hierarchy
  Memory is slow, exploit spatial and temporal locality for performance

## Slide 5: A Modern Memory Hierarchy
Register File, 32 words, sub-nsec
L1 Cache, ~32 KB, ~nsecs
L2 cache, 512KB – 1 MB, ~nsecs
L3 Cache, ~ 10 nsecs
Main memory (DRAM), GB, ~100 ns
Disk, 100 GB, ~10 msec

## Slide 6: The guts of most interesting stuff is often ~this
void Foo(float* const A, float* const B, float* const C, const int M, const int N, const int K)
{
  for (int m = 0; m < M; m++) {
    for (int n = 0; n < N; n++) {
      for (int k = 0; k < K; k++) {
        C[m * M + n] += A[m * M + k] * B[k * K + n];
      }
    }
  }
}
And these are huge
Lab2: image.tif
480x640 pixels * 4 bytes/float ~= 1.3 MB (greyscale!)
Notes: Not literally these loops, but multi-dimensional math, which boils down to loops of basic op’s marching through arrays

## Slide 7: Cache

## Slide 8: Cache
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 9: Cache hierarchy vocabulary
Cache hit: When data needed by CPU is in the cache
Cache miss: When data needed by CPU is not in the cache
  Cache controller must fetch data into cache and return it to CPU
  Compulsory miss, conflict miss, capacity miss
  THRASHING
Cache tag
Cache valid
Evict
Cache block or Cache Line

## Slide 10: Locality and cacheing
Memory hierarchies exploit locality by cacheing (keeping close to the processor) data likely to be used again.
This is done because we can build large, slow memories and small, fast memories, but we can’t build large, fast memories.
If it works, we get the illusion of SRAM access time with disk capacity
SRAM access times are ~1ns at cost of $2000 to $5000 per Gbyte.
DRAM access times are ~70ns at cost of $20 to $75 per Gbyte.
Disk access times are 5 to 20 million ns at cost of $.20 to $2 per Gbyte.
Notes: DMT: I can’t remember if I checked this data recently. May be obsolete.

## Slide 11: A typical memory hierarchy
CPU
memory
memory
memory
memory
on-chip caches
off-chip cache
main memory
disk
small
expensive $/bit
cheap $/bit
big
so then where is my program and data??
fast
slow
memory
Notes: DMT: I keep this structure, even though off-chip caches are less common. But they are a possibility, and not non-existent. But I do mention they are rare now (used to be required)

## Slide 12: Cache Fundamentals
cpu
lowest-level
cache
next-level
memory/cache
Notes: DMT: I do spend a fair amount of time on next few slides.

## Slide 13: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cpu
lowest-level
cache
next-level
memory/cache

## Slide 14: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cache miss -- an access which isn’t
cpu
lowest-level
cache
next-level
memory/cache

## Slide 15: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cache miss -- an access which isn’t
hit time -- time to access the cache
cpu
lowest-level
cache
next-level
memory/cache

## Slide 16: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cache miss -- an access which isn’t
hit time -- time to access the cache
miss penalty -- time to move data from further level to closer
cpu
lowest-level
cache
next-level
memory/cache

## Slide 17: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cache miss -- an access which isn’t
hit time -- time to access the cache
miss penalty -- time to move data from further level to closer
hit ratio -- percentage of time the data is found in the cache
cpu
lowest-level
cache
next-level
memory/cache

## Slide 18: Cache Fundamentals
cache hit -- an access where the data is found in the cache.
cache miss -- an access which isn’t
hit time -- time to access the cache
miss penalty -- time to move data from further level to closer
hit ratio -- percentage of time the data is found in the cache
miss ratio -- (1 - hit ratio)
cpu
lowest-level
cache
next-level
memory/cache
Notes: I usually try and get them to figure out why architects prefer miss ratio (scales with performance better than hit ratio)

## Slide 19: Cache Fundamentals, cont.
cache block size or cache line size– the amount of data that gets transferred on a cache miss.
cpu
lowest-level
cache
next-level
memory/cache
Notes: DMT: architects are really bad about having multiple names for things. It’s tempting to simplify and consistently stick to a single term, but then they go out and hear the other and don’t know what it means.

## Slide 20: Cache Fundamentals, cont.
cache block size or cache line size – the amount of data that gets transferred on a cache miss.
instruction cache – cache that only holds instructions.
cpu
lowest-level
cache
next-level
memory/cache

## Slide 21: Cache Fundamentals, cont.
cache block size or cache line size – the amount of data that gets transferred on a cache miss.
instruction cache – cache that only holds instructions.
data cache – cache that only caches data.
cpu
lowest-level
cache
next-level
memory/cache

## Slide 22: Cache Fundamentals, cont.
cache block size or cache line size – the amount of data that gets transferred on a cache miss.
instruction cache – cache that only holds instructions.
data cache – cache that only caches data.
unified cache – cache that holds both.
cpu
lowest-level
cache
next-level
memory/cache

## Slide 23: Cacheing Issues
On a memory access -
  How do I know if this is a hit or miss?
On a cache miss -
  where to put the new data?
  what data to throw out?
  how to remember what data this is?
cpu
lowest-level
cache
next-level
memory/cache
access
miss

## Slide 24: Hardware implications on cache design
Caches are basically the thing that make real workloads fast
The size of a cache is inversely proportional to its speed
  Smaller caches are faster
And every bit counts
This is why caches use as few bits as possible to do their work
  This makes caches tricky to walk through as a human

## Slide 25: A simple cache
A cache that can put a line of data anywhere is called __________________________
The most popular replacement strategy is LRU ( ).
tag
data
the tag identifies
the address of
the cached data
4 entries, each block holds one word, any block
can hold any word.
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: DMT: I walk through these examples slowly. For each address, finding the index bits and tag bits and recording hit or miss, and updating the cache picture.
“fully associative”
“least recently used”
(I know these answers are elementary for you, but you’ll be amazed what you can forget when you’re in front of a crowd, so it’s good to keep notes on even the most basic things)

## Slide 26: A simple cache
A cache that can put a line of data anywhere is called Fully Associative
The most popular replacement strategy is LRU ( Least Recently Used ).
tag
data
the tag identifies
the address of
the cached data
4 entries, each block holds one word, any block
can hold any word.
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: DMT: I walk through these examples slowly. For each address, finding the index bits and tag bits and recording hit or miss, and updating the cache picture.
“fully associative”
“least recently used”
(I know these answers are elementary for you, but you’ll be amazed what you can forget when you’re in front of a crowd, so it’s good to keep notes on even the most basic things)

## Slide 27: A simpler cache
A cache that can put a line of data in exactly one place is called __________________.
Advantages/disadvantages vs. fully-associative?
an index is used
to determine
which line an address
might be found in
4 entries, each block holds one word, each word
in memory maps to exactly one cache location.
00000100
tag
data
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: “direct mapped”

## Slide 28: A simpler cache
A cache that can put a line of data in exactly one place is called direct mapped
Advantages/disadvantages vs. fully-associative?
an index is used
to determine
which line an address
might be found in
4 entries, each block holds one word, each word
in memory maps to exactly one cache location.
00000100
tag
data
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: “direct mapped”

## Slide 29: A set-associative cache
A cache that can put a line of data in exactly n places is called n-way ______________________.
The cache lines/blocks that share the same index are a cache ____________.
tag
data
4 entries, each block holds one word, each word
in memory maps to one of a set of n cache lines
00000100
tag
data
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: DMT: they’re starting to get the idea, but pretty important to illustrate associativity.
“set”

## Slide 30: A set-associative cache
A cache that can put a line of data in exactly n places is called n-way set-associative.
The cache lines/blocks that share the same index are a cache set.
tag
data
4 entries, each block holds one word, each word
in memory maps to one of a set of n cache lines
00000100
tag
data
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
Notes: DMT: they’re starting to get the idea, but pretty important to illustrate associativity.
“set”

## Slide 31: Longer Cache Blocks
Large cache blocks take advantage of spatial locality.
Too large of a block size can waste cache space.
Longer cache blocks require less tag space
tag
data
4 entries, each block holds two words, each word
in memory maps to exactly one cache location
(this cache is twice the total size of the prior caches).
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
00000100
Notes: DMT: by this one, we may be stretching their patience. So I do want to get the big concept across (ie, showing how you can get a hit on first access to a word), but may otherwise go through this one a little more quickly.

## Slide 32: Longer Cache Blocks
Large cache blocks take advantage of spatial locality.
Too large of a block size can waste cache space.
Longer cache blocks require less tag space
tag
data (now 64 bits)
4 entries, each block holds two words, each word
in memory maps to exactly one cache location
(this cache is twice the total size of the prior caches).
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
00000100
Notes: DMT: by this one, we may be stretching their patience. So I do want to get the big concept across (ie, showing how you can get a hit on first access to a word), but may otherwise go through this one a little more quickly.

## Slide 33: Q: Describing Cache Type Tradeoffs?
Selection | Fully-Associative | 4-way Set Associative | Direct Mapped
A | 3 | 2 | 1
B | 3 | 3 | 2
C | 1 | 2 | 3
D | 3 | 2 | 1
E | None of the above |  | 
Exceptional usage of the cache space in exchange for a slow hit time
Poor usage of the cache space in exchange for an excellent hit time
Reasonable usage of cache space in exchange for a reasonable hit time
Notes: Correct Answer - C

## Slide 34: Back to Block Size
If block size increases spatial locality, should we just make the cache block size really, really big????

## Slide 35: Block Size and Miss Rate

## Slide 36: Cache Parameters
Cache size = Number of sets * block size * associativity
tag
data
tag
data
Bytes per block
Blocks per set
Sets per Cache
Warning / Notice—Things that count towards “cache size”: cache data
Things that do not count towards “cache size”: tags, valid bits, etc…
Notes: DMT: I really try and push the idea that caches are three dimensional entities, and best understood that way, and size is just the product of the three.
Oh, and by the way, it is not obvious to them that “cache size” only counts the data array (not tags, metadata, etc.), so need to emphasize that.

## Slide 37: Cache Parameters
Cache size = Number of sets * block size * associativity
tag
data
tag
data
Bytes per block
Blocks per set
Sets per Cache
Warning / Notice—Things that count towards “cache size”: cache data
Things that do not count towards “cache size”: tags, valid bits, etc…
Is this very confusing?
Yes, until you implement one.
It is what the world has settled on, so you need to know this and become comfortable with it.
Notes: DMT: I really try and push the idea that caches are three dimensional entities, and best understood that way, and size is just the product of the three.
Oh, and by the way, it is not obvious to them that “cache size” only counts the data array (not tags, metadata, etc.), so need to emphasize that.

## Slide 38: Cache Parameters
Cache size = Number of sets * block size * associativity
128 blocks, 32-byte block size, direct mapped, size = ?
128 KB cache, 64-byte blocks, 512 sets, associativity = ?
(always keep in mind “cache size” only counts the data storage)

## Slide 39: Q: How many bits for each field?
tag index block offset
N-bit address
Generally, we have variables block_size, cache_size, and memory_size
  Let’s work it out for
    BS = 8 bytes
    CS = 1 KB
    MS = 4 MB
  And we have a 4-way set-associative cache?
What is the…
  Number of bits for the block offset: ____
  Number of bits for the index: ____
  Number of bits for the tag: ____
Notes: Correct Answer - C
DMT: In the past, I usually haven’t given them the formulas. I prefer to just reason about them. “need to choose between 256 sets, so must be log 256, or 8 bits”. This kind of hits the middle ground. They get the formulas here, but don’t show up in their permanent notes (since clicker questions don’t go in the slides I post).

## Slide 40: Q: How many bits for each field?
tag index block offset
N-bit address
Generally, we have variables block_size, cache_size, and memory_size
  Let’s work it out for
    BS = 32 bytes
    CS = 16 KB
    MS = 8 MB
  And we have a 8-way set-associative cache?
What is the…
  Number of bits for the block offset: ____
  Number of bits for the index: ____
  Number of bits for the tag: ____
Notes: Correct Answer - C
DMT: In the past, I usually haven’t given them the formulas. I prefer to just reason about them. “need to choose between 256 sets, so must be log 256, or 8 bits”. This kind of hits the middle ground. They get the formulas here, but don’t show up in their permanent notes (since clicker questions don’t go in the slides I post).

## Slide 41: Handling a Cache Access
1. Use index and tag to access cache and determine hit/miss.
2. If hit, return requested data.
3. If miss, select a cache block to be replaced, and access memory or next lower cache (possibly stalling the processor).
  load entire missed cache line into cache
  return requested data to CPU (or higher cache)
4. If next lower memory is a cache, goto step 1 for that cache.

## Slide 42: Accessing a Sample Cache
64 KB cache, direct-mapped, 32-byte cache block size
31 30 29 28 27 .......... 17 16 | 15 14 13 12 11 10 9 8 7 6 5 | 4 3 2 1 0
tag
index
valid
tag
data
64 KB / 32 bytes =
2 K cache blocks/sets
11
=
256
32
16
hit/miss
0
1
2
...
...
...
...
2045
2046
2047
block offset

## Slide 43: Accessing a Sample Cache
32 KB cache, 2-way set-associative, 16-byte block size
31 30 29 28 27 .......... 17 16 15 14 | 13 12 11 10 9 8 7 6 5 4 | 3 2 1 0
tag
index
valid
tag
data
32 KB / 16 bytes / 2 =
1 K cache sets
10
=
18
hit/miss
0
1
2
...
...
...
...
1021
1022
1023
block offset
tag
data
valid
=

## Slide 44: Cache Alignment
The data that gets moved into the cache on a miss are all data whose addresses share the same tag and index (regardless of which data gets accessed first).
This results in
  no overlap of cache lines
  easy mapping of addresses to cache lines (no additions)
  data at address X always being present in the same location in the cache block (at byte X mod blocksize) if it is there at all.
Think of main memory as organized into cache-line sized pieces (because in reality, it is!).
tag index block offset
memory address
.
.
.
0
1
2
3
4
5
6
7
8
9
10
.
.
.
Memory
Notes: DMT: another thing not nearly as obvious to them as it is to us.

## Slide 45: How does the cache actually connect to the execution core?
This is a “standard, five stage pipeline”
For machines with no caches, the “DM” looks more like this:
IM
Reg
ALU
DM
Reg
ALU
DM
Memory Interface Module
Address
Data
Read?
Write?
Data

## Slide 46: How does the cache actually connect to the execution core?
This is a “standard, five stage pipeline”
For machines with no caches, the “DM” looks more like this:
IM
Reg
ALU
DM
Reg
ALU
DM
Memory Interface Module
Address
Data
Read?
Write?
Data
Stall
DRAM Controller
DRAM
Other
Peripherals
Memory Bus

## Slide 47: How does the cache actually connect to the execution core? [ Simplified View! Very different between embedded & high-perf! ]
ALU
DM
Memory Interface Module
Address
Data
Read?
Write?
Data
Stall
DRAM Controller
DRAM
Other
Peripherals
Memory Bus

## Slide 48: How does the cache actually connect to the execution core? [ Simplified View! Very different between embedded & high-perf! ]
ALU
DM
Memory Interface Module
Address
Data
Read?
Write?
Data
Stall
DRAM Controller
DRAM
Other
Peripherals
Memory Bus
Cache(s)

## Slide 49: How does the cache actually connect to the execution core? [ Simplified View! Very different between embedded & high-perf! ]
ALU
DM
Memory Interface Module
Address
Data
Read?
Write?
Data
Stall
DRAM Controller
DRAM
Other
Peripherals
Memory Bus
L1 Cache
A real interface (from a simple design)

## Slide 50: Cache Alignment Revisited
The data that gets moved into the cache on a miss are all data whose addresses share the same tag and index (regardless of which data gets accessed first).
Think of main memory as organized into cache-line sized pieces (because in reality, it is!).
“Block-aligned” access is similar to the “word-aligned” access you have been thinking about already
  Core <> Cache interface: Word aligned
  Cache <> Mem interface: Block aligned
tag index block offset
memory address
.
.
.
0
1
2
3
4
5
6
7
8
9
10
.
.
.
Memory
Notes: DMT: another thing not nearly as obvious to them as it is to us.

## Slide 51: When executing code, what does all this have to do with performance and alignment?
IM
Reg
ALU
DM
Reg
Notes: Draw out the simplified view, DM <> Cache to make the hit time point, Cache <> Memory to make the alignment point

## Slide 52: Which of the following things are possible?
Selection | Fully-Associative | 4-way Set Associative | Direct Mapped
A | 3 | 2 | 1
B | 3 | 3 | 2
C | 1 | 2 | 3
D | 3 | 2 | 1
E | None of the above |  | 
It is possible to make a “set-associative” cache to hav N=1 sets?
It is possible for a set-associative cache to have N=3 sets?
It is possible for a cache to have a 12-byte block size?
Notes: Correct Answer - C

## Slide 53: Associative Caches
Higher hit rates, but...
longer access time
  (longer to determine hit/miss, more muxing of outputs)
more space (longer tags)
  16 KB, 16-byte blocks, DM, tag = ?
  16 KB, 16-byte blocks, 4-way, tag = ?
Notes: DMT: really savvy ones can be a bit skeptical here, knowing that simple muxes aren’t that big a deal. This is where I usually explain (going back to a previous picture) that the biggest difference is between DM and 2-way because with DM you can read the data immediately without waiting for the tag check. For n-way, you need to wait. Then the incremental cost 2-way, 3-way, 8-way, etc. is much smaller after that.

## Slide 54
for (int i = 0; i < 10,000,000; i++)
sum += A[i];
Assume each element of A is 4 bytes and sum is kept in a register. Assume a baseline direct-mapped 32KB L1 cache with 32 byte blocks. Assume this loop is visited many times.
Which changes would help the hit rate of the above code?
Selection | Change
A | Increase to 2-way set associativity
B | Increase block size to 64 bytes
C | Increase cache size to 64 KB
D | A and C combined
E | A, B, and C combined
Notes: Correct Answer – B – HW flipped heads (stays the same)
Primary Purpose: Having students understand the impact of block size, cache size, and associativity
Concept: Aid students in understanding the interaction of caches and real code.
Expected mistakes: Not realizing set-associativity (A) and cache size (C) are irrelevant for streaming behavior
Post Discussion: Discuss how each improvement would change the cache behavior

## Slide 55
for (int i=0; i < 10,000,000; i++)
for (int j = 0; j < 8192; j++)
sum += A[j] – B[j];
Assume each element of A and B are 4 bytes.
Assume each array is at least 32KB in size.
Assume sum is kept in a register.
Assume a baseline direct-mapped 32KB L1 cache with 32 byte blocks.
Which changes would help the hit rate of the above code?
Selection | Change
A | Increase to 2-way set associativity
B | Increase block size to 64 bytes
C | Increase cache size to 64 KB
D | A and C combined
E | A, B, and C combined
Notes: Correct Answer - E
Expected mistakes: Not realizing (B) still helps for the first iteration if combined with A and C. Also – (A) is subtle. Because A and B are at least 32KB in size and the cache is 32KB – conflict misses are guaranteed. Depending on how the addresses are laid out, the two arrays MAY not conflict with a 64KB cache, but it is more likely that they would. 2-way associativity would guarantee they could each stay in the cache without conflicts.

## Slide 56: Dealing with Stores
Stores must be handled differently than loads, because...
  they don’t necessarily require the CPU to stall.
  they change the content of cache/memory (creating memory consistency issues)
Q: Can you think of a situation when you might need to load from memory before you can execute a store?
  Can you think of another one?
Notes: “read”
Two situations:
- Store byte/halfword on a word-architected machine
- Cache block > word

## Slide 57: Policy decisions for stores
Keep memory and cache identical?
  _____________________ => all writes go to both cache and main memory
  _____________________ => writes go only to cache. Modified cache lines are written back to memory when the line is replaced.
Make room in cache for store miss?
  write-allocate => on a store miss, bring written line into the cache
  write-around => on a store miss, ignore cache
Notes: “write-through”
“write-back”

## Slide 58: Dealing with stores
On a store hit, write the new data to cache.
  In a write-through cache, write the data immediately to memory.
  In a write-back cache, mark the line as dirty.
On a store miss, initiate a cache block load from memory for a write-allocate cache.
  Write directly to memory for a write-around cache.
On any kind of cache miss in a write-back cache, if the line to be replaced in the cache is dirty, write it back to memory.

## Slide 59: Cache Performance
CPI = BCPI + MCPI
  BCPI = base CPI, which means the CPI assuming perfect memory
  MCPI = the memory CPI, the number of cycles (per instruction) the processor is stalled waiting for memory.
MCPI = accesses/instruction * miss rate * miss penalty
  this assumes we stall the pipeline on both read and write misses, that the miss penalty is the same for both, that cache hits require no stalls.
  If the miss penalty or miss rate is different for Inst cache and data cache (common case), then
  MCPI = I$ accesses/inst x I$MissRate x I$MissPenalty
  + D$ accesses/inst x D$MissRate x D$MissPenalty

## Slide 60: In fact…
Can generalize this “formula” further for other stalls
  (This is just putting a label on the ”penalty” idea we introduced earlier)
CPI = BCPI + DHSPI + BHSPI + MCPI
  DHSPI = data hazard stalls per instruction
  BHSPI = branch hazard stalls per instruction.

## Slide 61: Cache Performance
Instruction cache miss rate of 4%
Data cache miss rate of 10%
BaseCPI = 1.0 (no data or control hazards)
20% of instructions are loads and stores
Miss penalty = 12 cycles
CPI = ???
Selection | CPI (rounded if necessary)
A | 1.24
B | 1.34
C | 1.48
D | 1.72
E | None of the above
Notes: CPI = 1 + %insts*%miss*miss_penalty
CPI = 1+(1.0)*.04*12 + .2*.10*12 = 1+ .48+.24 =1.72
Work out on next slide

## Slide 62: Cache Performance
Unified cache
25% of instructions are loads and stores
BaseCPI = 1.2, miss penalty of 10 cycles
If we improve the miss rate from 10% to 4% (e.g. with a larger cache), how much do we improve performance?

## Slide 63: Cache Performance
BaseCPI = 1
Miss rate of 8% overall, 20% loads, miss penalty 20 cycles, never stalls on stores.
What is the speedup from doubling the CPU clock rate?

## Slide 64: Example -- DEC Alpha 21164 Caches
21164 CPU
core
Instruction
Cache
Data
Cache
Unified
L2
Cache
Off-Chip
L3 Cache
ICache and DCache -- 8 KB, DM, 32-byte lines
L2 cache -- 96 KB, ?-way SA, 32-byte lines
L3 cache -- 1 MB, DM, 32-byte lines
Notes: DMT: It isn’t obvious that associativity doesn’t have to be power of 2 (for more struggling students, I guess, it’s not clear that the others must be!), so it’s good to get them to figure out why you can have a 96 kb cache (not a power of 2), as it’s a 3-way SA cache.
I use this example because this was the very first 2-level on-chip cache, and was a bit of an eye opener (actually the Jouppi paper that preceded the design). I like to talk about how a 2-level on chip cache, even when the technology is constant, still allows you to get fast access and low miss rate with one design. It’s also an opportunity to explain that cache access time is highly correlated with size.

## Slide 65: Three types of cache misses
Compulsory (or cold-start) misses
  first access to the data.
Capacity misses
  we missed only because the cache isn’t big enough.
Conflict misses
  we missed because the data maps to the same line as other data that forced it out of the cache.
tag
data
address string:
4 00000100
8 00001000
12 00001100
4 00000100
8 00001000
20 00010100
4 00000100
8 00001000
20 00010100
24 00011000
12 00001100
8 00001000
4 00000100
DM cache
Notes: Explain capacity vs. conflict as “would also occur in fully-associative cache with LRU”

## Slide 66: Q: Categorizing Misses
Suppose you experience a cache miss on a block (let's call it block A).
You have accessed block A in the past.
There have been precisely 1027 different blocks accessed between your last access to block A and your current miss.
Your block size is 32-bytes and you have a 64KB cache. What kind of miss was this?
Selection | Cache Miss
A | Compulsory
B | Capacity
C | Conflict
D | Both Capacity and Conflict
E | None of the above

## Slide 67: So, then, how do we decrease...
Compulsory misses?
Capacity misses?
Conflict misses?
Notes: DMT: I suppose if we’re really struggling with conversation in online classes, these could be turned into poll questions, etc. I much prefer open discussion, if possible.
The key here – does anyone in the class recognize that bigger caches are a solution to conflict misses?

## Slide 68: Cache Associativity

## Slide 69: LRU replacement algorithms
only needed for associative caches
requires one bit for 2-way set-associative, 8 bits (per set, 2/line) for 4-way, 24 bits for 8-way…
can be emulated with log n bits (NMRU)
can be emulated with use bits for highly associative caches (like page tables)
However, for most caches (eg, associativity <= 8), LRU is calculated exactly.
Notes: NMRU = not-most-recently-used

## Slide 70: Caches in Current Processors
Not long ago, they were DM at lowest level (closest to CPU), associative further away. Today they are less associative near the processor (2-4+), and more associative farther away (4-16).
split I and D close (L1) to the processor (for throughput rather than miss rate), unified further away (L2 and beyond).
write-through and write-back both common, but never write-through all the way to memory.
64-byte cache lines common (but getting larger)
Non-blocking
  processor doesn’t stall on a miss, but only on the use of a miss (if even then)
  this means the cache must be able to keep track of multiple outstanding accesses, even multiple outstanding misses.
Notes: Emphasize that splitting I/D L1 eliminates the IM/DM structural hazard

## Slide 71: Intel Nehalem (i7)
CPU
I$
D$
L2 cache
CPU
I$
D$
L2 cache
CPU
I$
D$
L2 cache
CPU
I$
D$
L2 cache
L3 cache
Instruction Cache
-32 KB, 4-way
-64-byte line
Data Cache
-32 KB, 8-way
-64-byte line
-write-back, write-allocate
Unified L2 Cache
-256 KB, 8-way
-64-byte line
-write-back, write-allocate
Shared, unified L3 Cache
-8 MB, 16-way
-64-byte line
-write-back, write-allocate

## Slide 72: What does PYNQ Provide?

## Slide 73: Key Points
Caches give illusion of a large, cheap memory with the access time of a fast, expensive memory.
Caches take advantage of memory locality, specifically temporal locality and spatial locality.
Cache design presents many options (block size, cache size, associativity, write policy) that an architect must combine to minimize miss rate and access time to maximize performance.

## Slide 74: Cache Extras
Additional Examples / Alternative Drawings

## Slide 75: Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 76: Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 77
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 78: Cache Concepts
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 79: Cache Concept Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 80: Types of Cache Implementation
Direct mapped cache
  Simple but lower spatial efficiency
  Fast
Fully associative cache
  Best spatial efficiency, complicated hardware design
  Slow
N-way set associative cache
  Frequently used in practice to balance trade-off between performance and complexity
  The cache is divided into groups of blocks, called sets.
  Each memory address maps to exactly one set in the cache, but data may be placed in any block within that set.

## Slide 81: Cache Abstraction & Metrics
Cache hit rate = #hits/#accesses
Average memory access time = #hit rate*hit latency + #miss rate* miss latency
Address
Tag Store
(Is this address in the cache? + bookkeeping)
Data Store (Stores memory blocks)
Hit/miss
Data

## Slide 82: Blocks and Addressing the Cache
Memory is logically divided into fixed size blocks
Each block maps to a location into the cache
  Determined by the index bits in the address
Cache access
  Use index bits to index to cache line
  Check valid stored in the stored tag
  Check tag bits against the tag stored in the tag store
If valid bit is true, and tag matches  cache hit
2b
3b
3b
tag
index
offset

## Slide 83: Direct Mapped Cache
Assume byte addressable memory, 256 bytes size of memory
8 byte blocks (block contains 8 bytes)  32 blocks
Assume cache 64 bytes;  8 blocks
2b
3b
3b
tag
index
offset
V | Tag
V | 
==/=!
Hit?
Data
Tag store
Data store

## Slide 84: Direct Mapped Cache Example
Let us assume memory is 64 bytes (assume it byte addressable).
How many address bits do we need?
Address bits of 6 (m=6) bits
Each block contains 4 bytes. What is the number of unique locations we can address ?

## Slide 85: Direct Mapped Cache Example
m = 6 & each block contains 4 bytes
What is the number of blocks ?
Number of blocks = 16
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15
16 | 17 | 18 | 19
60 | 61 | 62 | 63

## Slide 86: Direct Mapped Cache Example
m = 6 & each block contains 4 bytes
What is the number of blocks ?
Number of blocks = 16
What is the b (block offset)?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63

## Slide 87: Direct Mapped Cache Example
m = 6 & each block contains 4 bytes
What is the number of blocks ?
Number of blocks = 16
What is the b (block offset)?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
Block Size = 4 = 22  b = 2  The number of bits

## Slide 88: Direct Mapped Cache Example
m = 6 & each block contains 4 bytes
What is the number of blocks ?
Number of blocks = 16
What is the b (block offset)?
What is the value of l ?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
Block Size = 4 = 22  b = 2
 The number of bits
Block Offset (b=2)
Block Address (m-b)

## Slide 89: Direct Mapped Cache Example
Let us assume m = 6 & each block contains 4 bytes
What is the number of unique locations we can address ?
What is the number of blocks ?
What is the value of b ?
What is the value of l ?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
Block Size = 4 = 22  b = 2
 The number of bits
Block Offset (b=2)
Block Address (m-b)
0 | 1 | 2 | 3 | 0
4 | 5 | 6 | 7 | 1
8 | 9 | 10 | 11 | 2
12 | 13 | 14 | 15 | 3

## Slide 90: Direct Mapped Cache Example
Let us assume m = 6 & each block contains 4 bytes
What is the number of unique locations we can address ?
What is the number of blocks ?
What is the value of b ?
What is the value of l ?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
Block Size = 4 = 22  b = 2
 The number of bits
Block Offset (b=2)
Block Address (m-b)
0 | 1 | 2 | 3 | 0
4 | 5 | 6 | 7 | 1
8 | 9 | 10 | 11 | 2
12 | 13 | 14 | 15 | 3
#lines = 4 =22  l =2
Cache line
tag

## Slide 91: Direct Mapped Cache Example
Let us assume m = 6 & each block contains 4 bytes
What is the number of unique locations we can address ?
What is the number of blocks ?
What is the value of b ?
What is the value of l ?
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
Block Size = 4 = 22  b = 2
 The number of bits
Block Offset (b=2)
Block Address (m-b)
#lines = 4 =22  l =2
Cache line
tag
tag | 0 | 1 | 2 | 3 |  | 0
tag | 4 | 5 | 6 | 7 |  | 1
tag | 8 | 9 | 10 | 11 |  | 2
tag | 12 | 13 | 14 | 15 |  | 3

## Slide 92: Direct Mapped Cache Example
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 1 | 0 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
tag | 0 | 1 | 2 | 3 |  | 0
tag | 4 | 5 | 6 | 7 |  | 1
tag | 8 | 9 | 10 | 11 |  | 2
tag | 12 | 13 | 14 | 15 |  | 3

## Slide 93: Direct Mapped Cache Example
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 1 | 0 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
tag | 0 | 1 | 2 | 3 |  | 0
tag | 4 | 5 | 6 | 7 |  | 1
tag | 8 | 9 | 10 | 11 |  | 2
tag | 12 | 13 | 14 | 15 |  | 3

## Slide 94: Direct Mapped Cache Example
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 1 | 0 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
0 | 0 | 1 | 2 | 3
1 | 4 | 5 | 6 | 7
2 | 8 | 9 | 10 | 11
3 | 12 | 13 | 14 | 15
4 | 16 | 17 | 18 | 19
15 | 60 | 61 | 62 | 63
tag | 0 | 1 | 2 | 3 |  | 0
tag | 4 | 5 | 6 | 7 |  | 1
tag | 8 | 9 | 10 | 11 |  | 2
tag | 12 | 13 | 14 | 15 |  | 3

## Slide 95: 2-way set associative cache
MM = 64 bytes
CS = 32 bytes
BS = 4 bytes
Set size = 2 cache lines
#cache lines = CS/BS = 8
#sets = #cache lines/set size = 4
Block Offset (b=2)
Block Address (m-b)
set line
tag
2-way set associative cache
  Find the set
  Compare tag with the tags stored

## Slide 96: Types of Cache Implementation
Direct mapped cache
  Simple but low efficiency
Fully associative cache
  Has high efficiency, complicated hardware design
N-way set associative cache
  Frequently used in practice to balance trade-off between performance and complexity
  The cache is divided into groups of blocks, called sets.
  Each memory address maps to exactly one set in the cache, but data may be placed in any block within that set.

## Slide 97: Resources
Some of the slides are adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective; Third Edition

## Slide 98: Compiler Level Optimization

## Slide 99: Compiler Level Optimizations
Many of the optimizations can be done by manually by the programmer, and many of the optimizations (e.g., loop) that we will see can be done by compiler (compiler can be smart).
If compiler can optimize the program, compiler should do the job!
Sometimes, it is needed to understand these optimizations because of limitations of compiler

## Slide 100: Code Motion
Reduce frequency with which computation performed
  If it will always produce same result
  Especially moving code out of loop
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective
void set_row(double *a, double *b,​
long i, long n)​
{​
long j;​
for (j = 0; j < n; j++)​
a[n*i+j] = b[j];​
}
void set_row(double *a, double *b,
long i, long n)
{
long j;
int ni = n*i;
for (j = 0; j < n; j++)
a[ni+j] = b[j];
}

## Slide 101: Compiler Generated Code Motion
set_row:​ testq %rcx, %rcx # Test n​ jle .L1 # If 0, goto done​ imulq %rcx, %rdx # ni = n*i​ leaq (%rdi,%rdx,8), %rdx # rowp = A + ni*8​ movl $0, %eax # j = 0​ .L3: # loop:​ movsd (%rsi,%rax,8), %xmm0 # t = b[j]​ movsd %xmm0, (%rdx,%rax,8) # M[A+ni*8 + j*8] = t​ addq $1, %rax # j++​ cmpq %rcx, %rax # j:n​ jne .L3 # if !=, goto loop​ .L1: # done:​ rep ; ret
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective
long j;​​
for (j = 0; j < n; j++)​​
a[n*i+j] = b[j];​
long j;​
int ni = n*i;​
for (j = 0; j < n; j++) ​
a[ni+j] = b[j];

## Slide 102: Elimination (share) of Common Subexpressions
3 multiplications: i*n, (i–1)*n, (i+1)*n​
1 multiplication: i*n​
leaq 1(%rsi), %rax # i+1​
leaq -1(%rsi), %r8 # i-1​
imulq %rcx, %rsi # i*n​
imulq %rcx, %rax # (i+1)*n​
imulq %rcx, %r8 # (i-1)*n​
addq %rdx, %rsi # i*n+j​
addq %rdx, %rax # (i+1)*n+j​
addq %rdx, %r8 # (i-1)*n+j​
​
imulq %rcx, %rsi # i*n​
addq %rdx, %rsi # i*n+j​
movq %rsi, %rax # i*n+j​
subq %rcx, %rax # i*n+j-n​
leaq (%rsi,%rcx), %rcx # i*n+j+n​
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective
/* Sum neighbors of i,j */​
up = val[(i-1)*n + j ];​
down = val[(i+1)*n + j ];​
left = val[i*n + j-1];​
right = val[i*n + j+1];​
sum = up + down + left + right;
long inj = i*n + j;​
up = val[inj - n];​
down = val[inj + n];​
left = val[inj - 1];​
right = val[inj + 1];​
sum = up + down + left + right;

## Slide 103: Reduction in Strength
Replace costly operation with simpler one
  Shift, add instead of multiply or divide
  16*x --> x << 4
  * +
for (i = 0; i < n; i++) {​
int ni = n*i;​
for (j = 0; j < n; j++)​
a[ni + j] = b[j];​
}
int ni = 0;​
for (i = 0; i < n; i++) {​
for (j = 0; j < n; j++)​
a[ni + j] = b[j];​
ni += n;​
}

## Slide 104: Memory Aliasing
# sum_rows1 inner loop​
.L4:​
movsd (%rsi,%rax,8), %xmm0 # FP load​
addsd (%rdi), %xmm0 # FP add​
movsd %xmm0, (%rsi,%rax,8) # FP store​
addq $8, %rdi​
cmpq %rcx, %rdi​
jne .L4
  Code updates b[i] on every iteration​
  Extra store
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective
/* Sum rows is of n X n matrix a​
and store in vector b */​
void sum_rows1(double *a, double *b, long n) {​
long i, j;​
for (i = 0; i < n; i++) {​
b[i] = 0;​
for (j = 0; j < n; j++)​
b[i] += a[i*n + j];​
}​
}

## Slide 105: Memory Aliasing
  No extra store for intermediate result
# sum_rows2 inner loop​
.L10:​
addsd (%rdi), %xmm0 # FP load + add​
addq $8, %rdi​
cmpq %rax, %rdi​
jne .L10
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows2(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
double val = 0;
for (j = 0; j < n; j++)
val += a[i*n + j];
b[i] = val;
}
}

## Slide 106: Loop Interchange
Original loop:
for(j=0; j<M; j++)
for(i=0; i<N; i++)
A[i][j]=a[i][j]+b[i][j];
Interchanged loop:
for(i=0; i<N; i++)
for(j=0; j<M; j++)
c[i][j]=a[i][j]+b[i][j];
Improved locality

## Slide 107: Loop Fusion
Original loops:
for(i=0; i<N; i++)
a[i] = b[i] + 10
for(i=0; i<N; i++)
c[i] = a[i]*2
Fused loops:
for(i=0; i<N; i++){
a[i] = b[i] + 10
c[i] = a[i]*2
}
Notes: Loop fusion is merging two or more loops.

## Slide 108: Loop Fusion
Original loops:
for(i=0; i<N; i++)
a[i] = b[i] + 10
for(i=0; i<N; i++)
c[i] = a[i]*2
Fused loops:
for(i=0; i<N; i++){
a[i] = b[i] + 10
c[i] = a[i]*2
}
Reducing loop overhead
Increasing the amount of work done in a loop
Improving locality by combining loops that reference the same array
Notes: Loop fusion is merging two or more loops.

## Slide 109: Loop Distribution
It is opposite of loop fusion
Distributed loops:
for(i=0; i<N; i++)
a[i] = b[i] + 10
for(i=0; i<N; i++)
c[i] = a[i]*2
Original loops:
for(i=0; i<N; i++){
a[i] = b[i] + 10
c[i] = a[i]*2
}

## Slide 110: Loop Distribution
It is opposite of loop fusion
Distributed loops:
for(i=0; i<N; i++)
a[i] = b[i] + 10
for(i=0; i<N; i++)
c[i] = a[i]*2
Original loops:
for(i=0; i<N; i++){
a[i] = b[i] + 10
c[i] = a[i]*2
}
It can improve locality in multi-core processing
It can improve hardware prefetch by separating different data streams

## Slide 111: Loop Invariant Computations
Calculations that do not change between loop iterations
Can be moved outside a loop
Original loop:
for(i=0; i<N; i++)
a[i] = i* (SOME_NUMBER/100)
Transformed loop:
for(i=0; i<N; i++)
a[i] = i* funct();

## Slide 112: Loop Unrolling
void foo(
int A[8],
int B[8]) {
for(int i=0;i<8;i++){
B[i]=A[i]*3;
}
}
void foo(
int A[8],
int B[8]) {
for(int i=0;i<8; i+=2){
B[i]=A[i]*3;
B[i+1]=A[i+1]*3;
}
}
Increases ILP
To reduce loop overhead instructions
Increases code size

## Slide 113: Dead Code Elimination
int global;
void f ()
{
int i;
i = 1; /* dead store */
global = 1; /* dead store */
global = 2;
return;
global = 3; /* unreachable */
}
int global;
void f ()
{
global = 2;
return;
}

## Slide 114: Constant Folding
Evaluate constant expressions at compile time
Only possible when side-effect freeness guaranteed
Int a = 4+5;
Int a = 9;
true not;
false;
Caveat: Floating implementations could be different between machines
  -ffast-math (really -funsafe-math-optimizations) lets compiler ignore this

## Slide 115: Constant Propagation
Variables that have constant value, e.g. c := 3
  Later uses of c can be replaced by the constant
  If no change of c between!
Analysis needed, as b can be assigned more than once!
Int b = 3;
Int c = 1 + b;
Int d = b + c;
Int b = 3;
Int c = 1 + 3;
Int d = 3 + c;

## Slide 116: Compiler Optimization Passes
Loop Optimizations
  Loop fission
  Loop fusion
  Loop interchange
  Loop invariant code motion
  Loop unrolling
  …
Data Flow Optimizations
  Common subexpression elimination
  Constant folding and propagation
  Dead code elimination
  …
Code Generation Optimization
  Register Allocation
  Instruction Scheduling
  Instruction Selection
  Reordering computations
  ,…

## Slide 117: LLVM: Optimizing Compiler
LLVM is a compiler infrastructure designed as a set of reusable libraries with well defined interfaces
LLVM IR is target independent
https://www.aosabook.org/en/llvm.html
https://gcc.gnu.org/onlinedocs/gcc/Optimize-Options.html
LLVM IR
LLVM IR
LLVM IR
Optimization
Pass 1
Optimization
Pass 1
Optimization
Pass 1
…. . ….
LLVM IR
LLVM IR

## Slide 118: Compiler Optimization Passes
Loop Optimizations
  Loop fission
  Loop fusion
  Loop interchange
  Loop invariant code motion
  Loop unrolling
  …
Data Flow Optimizations
  Common subexpression elimination
  Constant folding
  Dead store elimination
  …
Code Generation Optimization
  Register Allocation
  Instruction Scheduling
  Instruction Selection
  Reordering computations
  ,…

## Slide 119: Optimizing Compilers
Provide efficient mapping of program to machine
  register allocation
  code selection and ordering (scheduling)
  dead code elimination
  ...
  eliminating minor inefficiencies
Do not optimize (usually) the "algorithm"
  up to programmer to select best overall algorithm for a given task
    Sorting: big-O(n2) vs. big-O(nlogn)
  big-O savings are (often) more important
Have difficulty overcoming inherent limitations (cache, inherent parallelism)

## Slide 120: Limitations of Optimizing Compilers
Operate under fundamental constraint
Must not cause any change in program behavior
Except, possibly when program making use of nonstandard language features
Behavior that may be obvious to the programmer can be obfuscated by languages and coding styles
e.g., Data ranges may be more limited than variable types suggest
Most analysis is performed only within procedures
Whole-program analysis is too expensive in most cases
Newer versions of GCC do interprocedural analysis within individual files
But, not between code in different files
Most analysis is based only on static information
Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative​
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective

## Slide 121: GCC O1, O2, O3 levels
-O1
-O2
-O3

## Slide 122: Inline Assembly
Ability to embed low level assembly code in high-level C/C++ code
__asm [volatile] (code); /* Basic inline assembly syntax */
  "ADD R0, R1, R2
Why use inline assembly ?

## Slide 123: Inline Assembly
Ability to embed low level assembly code in high-level C/C++ code
__asm [volatile] (code); /* Basic inline assembly syntax */
  "ADD R0, R1, R2
Why use inline assembly ?
  Optimization for codes that can not be naturally expressed by high-level languages
    Reversing bits
  Access to professor specific instructions
    NEON
  System class